## Slide 1: Integrated course „Energy Economics“ - Natural Gas Markets
Chair of Energy Systems
Prof. Dr. Boris Heinz | Dr. Elena Timofeeva
elena.timofeeva@tu-berlin.de

## Slide 2: Outline
Natural gas reserves and production
Long distance gas pipelines
Gas storage
LNG markets
Wholesale markets for natural gas
Retail gas markets

## Slide 3: Gaseous Fuels
Natural gas – mainly methane
  H gas – high-calorific natural gas (higher CH4 content → heat value)
  L gas – low-calorific natural gas (produced in GE &NL)
Liquefied petroleum gas (LPG) – mainly propane and butane, byproduct of oil refinery process
Town gas (cooking gas) – byproduct of coke plants

## Slide 4: Properties of Gaseous Fuels
© Prof. Dr. Georg Erdmann
Notes: Latent heat of vaporisation of water vapour. Same types of fuel are compared by HHV, different types of fuel – by LHV (due to different hydrogen content).

## Slide 5: Natural gas
Conventional natural gas
Extracted from gas deposits by conventional means
Associated gas – released during oil extraction (often flared but can be utilised)
Unconventional natural gas
Shale gas (>1000 m deep) – extracted by fracking
Coal bed methane – found in coal formations (300-1000 m deep)
Methane hydrates – found on ocean seabed

## Slide 6: Natural gas value chain

## Slide 7: Global Gas Resources
Source: BGR, 2013
Resources are all useful raw materials available in nature.
Reserves are resources existing with high probability and economically feasible for extraction.

## Slide 8: Reserves and extraction of natural gas
Source: Zweifel / Praktiknjo / Erdmann (2017) after BP (2014)
*
The Persian Gulf and the Caspian Sea areas
  (Bahrain, Iran, Iraq, Kuwait, Oman, Qatar, Saudi Arabia, Syria, UAE, Yemen, other Middle East;
  Azerbaijan, Kazakhstan, Russia, Turkmenistan, Uzbekistan, other Europe & Eurasia)

## Slide 9: LNG imports by source (billion cubic meters)
Source: BP Statistical Review of World Energy 2019

## Slide 10: For reference: LNG imports Japan vs China 2018
Source: BP Statistical Review of World Energy 2019
Pipeline imports | 47,9
LNG imports | 73,5
Total imports | 121,3
Primary energy: consumption by fuel [million toe]
 | Oil | Natural gas | Coal | Nuclear | Hydro | RE | Total
Japan | 182,4 | 99,5 | 117,5 | 11,1 | 18,3 | 25,4 | 454,1
China | 641,2 | 243,3 | 1906,7 | 66,6 | 272,1 | 143,5 | 3273,5
Source: BP, 2019
Source: U.S. Energy Administration, based on China National Bureau of Statistics and IHS Markit
Natural gas:
Inter-regional trade
China [billion cubic metres]

## Slide 11: Natural Gas in the EU
© Prof. Dr. Georg Erdmann

## Slide 12: German Gas Imports
© Prof. Dr. Georg Erdmann
Source: BAFA, 2015
[TJ]

## Slide 13: Economics of Gas Pipelines
© Prof. Dr. Georg Erdmann
Throughput is the volume of gas passing through a pipeline in a period of time.
[m3/h]
Pipeline capacity is the maximum throughput.

## Slide 14: Game Theory: Double Marginalisation
© Prof. Dr. Georg Erdmann
Gas producer is able to infer on the import price resulting from gas importer’s optimisation based on the domestic demand curve. It then optimises its profit at the given import price.

## Slide 15: Monopoly Pricing

## Slide 16: Retail Gas Price set by the Monopolistic Gas Importer
© Prof. Dr. Georg Erdmann
Importer’s marginal cost = import price
(neglecting other cost elements)
Willingness to pay for the first unit = max. retail price
Linear demand function

## Slide 17: Game Theoretical View of the Gas Importer
© Prof. Dr. Georg Erdmann

## Slide 18: Game Theoretical View of the Pipeline Operator
© Prof. Dr. Georg Erdmann

## Slide 19: Solution under “Cooperation”
© Prof. Dr. Georg Erdmann

## Slide 20: Decision of the Pipeline Investor
© Prof. Dr. Georg Erdmann

## Slide 21: Transportation Cost of Hydrocarbons
Source: Zweifel / Praktiknjo / Erdmann, 2017

## Slide 22: LNG Process Chain
Source: BV 2009 / GIIGNL
Boiling point of methane −162 °C (−259.6 °F)
Approx. 600 times volume reduction
Source: Osaka Gas

## Slide 23: Major LNG Trading Flows in 2018
Source: GIIGNL, 2019
EXPORT
IMPORT
Algeria
Australia
Brunei
Indonesia
Malaysia
Nigeria
Oman
Papua New Guinea
Quatar
Russia
UAE
USA
China
France
India
Italy
Japan
Mexico
Pakistan
Singapore
South Korea
Spain
Taiwan
Thailand
Turkey
United Kingdom
2 - 3 MT
3 - 5 MT
5 - 10 MT
>10 MT

## Slide 24: LNG Flows in 2018

## Slide 25: Cost Structure of LNG Process Chain
Source: Zweifel / Praktiknjo / Erdmann (2017), after Cayrade (2014)
Liquefaction plant: | 
Investment outlay | 900M €
Operating expenses | 0,04 €/m3
LNG tanker fleet | e.g. 2 vessels á 135T t each
Investment outlay | 360M €
Operating expenses | 0,014 €/m3
Regasification plant w. storage | e.g. 80T m3 (Cartagena)
Investment outlay | 320M €
Operating expenses | 0,015 €/m3
Own gas requirement | 1/3 of transported gas

## Slide 26: Cost Comparison of LNG Projects
Source: Songhurst, OIES, 2018

## Slide 27: LNG Impact on Global Gas Markets
LNG trade leads to integration of regional gas markets
LNG supply chain is more flexible
LNG helps to develop more remote gas fields
Diversification helps mitigate the holdup problem
Source: Zweifel / Praktiknjo / Erdmann, 2017

## Slide 28: Gas storage technologies
Source: E.ON Ruhrgas
Station
Station
Observation well
Aquifer/
Production field
Porous rock storage
Cavern storage

## Slide 29: Gas storage facilities: Underground
Porous rock storage
  uses existing geological underground formations (e.g. depleted oil and gas fields, aquifers)
  relatively inexpensive (but higher investment costs for aquifers)
  large storage volume
  more cushion gas required
  low injection and withdrawal rate
Cavern storage
  artificial hollows carved out in underground rock or salt formations
  higher investment
  less cushion gas required
  higher withdrawal rate
  fast switching between injection and withdrawal mode
  provide short-term flexibility

## Slide 30: Gas storage facilities: Above ground
LNG storage
Insulated tanks at LNG terminals
No cushion gas needed
High injection/withdrawal rates
Gas tanks
Law or high pressure
Not economical for high volumes
Local storage
Line pack
Gas stored inside pipeline through increased pressure
Used to balance daily demand fluctuations

## Slide 31: Gas storage facilities in Germany
Max. usable working gas volume as of 31.12.2018, in TWh
Total
33 storage facilities
Cavern storage
17 facilities
Porous rock storage
15 facilities
Other
1 facility
H-Gas
29 facilities
L-Gas
4 facilities
BNetzA, 2019

## Slide 32: Merchant Use of a Gas Storage
© Prof. Dr. Georg Erdmann

## Slide 33: German gas storage: Filling level development
Source: BNetzA, 2019
Range of storage filling level since 04/2011
Filling level for current storage year – as of 1 Nov 2019
Storage year 2018/19 – compared to previous years
[%]

## Slide 34: Value of gas storage
Storage buffers supply and (daily & seasonally fluctuating) demand
Value of storage is determined by the cost of alternative sources of flexibility (transportation and capacity charges):
production swing, take-or-pay, interruptible contracts, spot market
Intrinsic value
  ability to inject a certain amount of gas in summer and withdraw it in winter
  price during withdrawal minus price during injection, i.e. seasonal spread
Extrinsic value
  ability to utilise the storage volume more than once (inject and withdraw gas) during the season to profit from short-term price volatility

## Slide 35: Third-Party Access to Gas Infrastructure
Non-discriminatory (effective and transparent) access to gas transportation systems is a crucial prerequisite for a liquid market for natural gas.
Unbundling for gas TSOs (see EU Gas Directive 2009/73/EC):
Transmission and distribution activities are separated from the rest of the value chain
Ownership unbundling
Independent system operator (ISO)
Independent transmission operator (ITO)
Certification to ensure compliance with unbundling requirements for transmission system owner or TSO controlled by person(s) from third country(ies)
„Gazprom clause“
See lecture 10
on unbundling: equivalent rationale and requirements apply for the gas sector.

## Slide 36: Gas Network Access Models
Point-to-point system
gas traders book specific transportation route from an entry to an exit point
distance-based or flatrate fee
Entry-exit system
entry and exit capacities are booked separately
entry fee and exit fee – no distance-related fee
traders with entry capacities can sell gas to traders with exit capacities
each exit point can be supplied from any entry point
Entry-exit system enables wholegas gas trading on virtual trading point (virtual hub) / market area level: gas is traded independently of its location in a market area.

## Slide 37: European gas regions, markets and hubs
Source: OIES (2017) with reference to www.worldatlasbook.com and P. Heather