## Slide 1: Integrated course „Energy Economics“ - Electricity Grid -
Chair of Energy Systems | Department of Energy Systems
Technische Universität Berlin

## Slide 2: Outline
Electricity grid (continued)
  Congestion management
  Grid access
  Grid tariff regulation
  Security of supply
Retail markets

## Slide 3: Congestion management
Congestion management relieves expected grid bottlenecks due to limited transmission capacity by correcting (cost-based) power plant dispatch decisions.
Countertrading
TSO counter-trades against the flow of congestion between bidding zones.
Redispatch
ramping up certain power plants while ramping down certain other power plants
Feed-in management (Einsman)
ramping down renewable power plants
Grid reserve
power plants kept available for service but not operational
against remuneration

## Slide 4: Redispatch: example
Source: Next Kraftwerke
TSO
Temporary
grid bottleneck
Power plant 1
Power plant 2
ramps up
ramps down

## Slide 5: Rising redispatch cost 2010-2018
© NODES, E-Bridge and Pöyry
Source: BNetzA

## Slide 6: Automatic frequency control
Automatic low frequency demand disconnection scheme
Source: VNN VDE
Frequency
Load to be diconnected
Disconnecting load is not required at this level.
Minimum required % of load to be disconnected

## Slide 7: Grid restoration
Grid operator coordinates grid restoration after a black-out by step-by-step activation of generation units and matching (appropriate) loads.
Blackstart capability: while most power plants require electricity to get running after a black-out, certain generation units are able to start operation when disconnected from the grid.
Associated costs for blackstart capability provider:
Maintenance
Regular tests
Personnel and training
Documentation

## Slide 8: Access to electrical grids
Grid operation is a natural monopoly, as network infrastructure is prohibitively costly to replicate.
As any monopoly, it is prone to eliminating newcomers (potential competition for affiliated generation/retail unit) by overcharging or denying technical feasibility.
Non-discrimination
Transparency
Cost recovery
Cost reflectiveness
Grid is an essential facility.
→ non-discriminatory third-party access
Source: Lévêque, 2010
Notes: Economies of scale: single firm can transport any amount of electricity at least cost.

## Slide 9: Electrical grid as a natural monopoly
Source: Zweifel / Erdmann / Praktiknjo, 2017
Notes: Average cost declines with rising quantity.
Downward sloping demand function (vs. price-taker under perfect competition)
Average revenue = price
Marginal revenue is always less than the price.
Increased amount tends to increase total revenue; the lower price tends to decrease total revenue.
Marginal revenue curve lies below demand curve.
Profit maximisation: Quantity at which marginal revenue equals marginal cost. Price corresponding to that quantity on the demand curve.

## Slide 10: Grid tariff regulation: Regulation approaches
Cost-based
Regulation approach
Incentive-based
Cost-plus:
a pre-defined profit margin is added to the costs
Rate-of-return:
a pre-defined rate of return on the regulatory asset base is guaranteed.
RAB is determined by amount of invested capital and cost of capital.
Revenue cap:
if higher profit realised within allowed revenues, the regulated entity keeps it.
Price cap:
max. prices (per unit) are determined for the regulatory period
Quality regulation: indicators for service quality and reliability
Notes: Water wheel converts kinetic energy of water is converted into mechanical movement.

## Slide 11: Averch-Johnson effect (1)
© Prof. Dr. Georg Erdmann
Notes: Principle-agent problem

## Slide 12: Averch-Johnson effect (2)
© Prof. Dr. Georg Erdmann

## Slide 13: Incentive regulation in Germany
5-year regulatory period (current period 2019-2024)
Revenue that TSO/DSO is allowed to earn is fixed for the regulatory period at a level.
Revenue cap: total cost + depreciation + return on equity
Investment costs into grid extension are allowed above cap.
Costs:
permanently non-controllable
temporarily non-controllable
controllable
volatile
Efficiency benchmarking – based on cost examination and structural data validation of individual TSO/DSO
The most efficient entity serves as benchmark.

## Slide 14: Incentive Regulation
Revenue costs
Revenue with anticipated cost reductions
Revenue without anticipated cost reductions
Tariff regulation
Time
© Prof. Dr. Georg Erdmann

## Slide 15: Incentive Regulation in Germany (cont.)
Source: CEER/BNetzA (2014)

## Slide 16: Composition of grid tariffs
O&M
Grid extension
Control power (capacity component)
Feed-in management (Einsman)
Redispatch
Grid reserve
Capacity reserve
Security reserve (coal/climate reserve)
Reactive power
Grid losses
Other

## Slide 17: Cost allocation of control power
© Prof. Dr. Georg Erdmann

## Slide 18: Grid tariffs structure
Source: BNetzA, 2015
Cost/revenues of grid level
Grid tariffs
transferred cost
own cost of
Grid level
revenues
total annual cost (€/kW)
simultaneity factor
HV
HV/MV
MV
MV/LV
LV
energy
price (AP)
power
price (LP)
basis
price (BP) (household consumers)
divided by annual Pmax (kW)
Total annual cost
LV without power measuring
Starting point
Starting from the highest voltage level, part of the grid costs (based on that level’s aggregated annual consumption peak – Pmax) are paid by grid users connected to that grid level. The residue is transferred to the next voltage level and distributed after the same logic – etc.
Notes: Grid tariffs are determined top-down for each grid level.

## Slide 19: Simultaneity (diversity) function
Grid users with low FLH pay lower power price (PP) and higher energy price (EP)
Grid users with high FLH pay higher PP and lower EP
Source: BNetzA, 2015
FLH | PP [€/kW*a] | EP [ct/kWh]
< 2.500 | a | x
> 2.500 | b | y
Annual grid fee:
EP * annual consumption + PP * Pmax
Pmax: annual peak load

## Slide 20: Security of supply indicators
ENS – Energy Not Served – amount of demand not served
LLD – Loss of Load Duration – number of hours of ENS
LOLE – Loss of Load Expectation
SAIDI – System Average Interruption Duration Index
SAIFI – System Average Interruption Frequency Index
MAIFI – Momentary Average Interruption Frequency Index
ENTSO-E Mid-term adequacy forecast
ni : no. of customers affected by interruption i
ti : duration of interruption i [min]
N : no. of customers
U : no. of interruptions
Notes: Unplanned interruptions

## Slide 21: SAIDI – System Average Interruption Index
Source: CEER, 2018
Unplanned SAIDI, including exceptional events (minutes per customer)
(2002 or later – 2016)

## Slide 22: Security of supply indicators
Cost
Quality
Grid cost
Value of lost load (VoLL)
Total cost
Source: E-Bridge, ZEW & FGH (2020)
Notes: Unplanned interruptions

## Slide 23: Recap: Electricity market structure types
Single buyer
Power pool
Free wholesale competition
Fully liberalised market with retail competition

## Slide 24: Electricity market structures: Single buyer

## Slide 25: Electricity market structures: Power pool

## Slide 26: Electricity market structures: Wholesale competition

## Slide 27: Electricity market structures: Retail competition

## Slide 28: Electricity retail under different market structures
Single buyer → regulated retail prices
Power pool → regulated retail prices;
Free wholesale competition
Fully liberalised market → retail competition
                unregulated retail prices
large consumers may be eligible to participate in the wholesale market

## Slide 29: Retail competition
The ultimate rationale of liberalisation/restructuring of the electricity sector is the prospect of lower prices for electricity consumers achievable through competition.
The option for final customer to switch supplier creates a competitive pressure for market players along the electricity supply chain.

## Slide 30: Categories of suppliers in the German market
Large vertically integrated utilities: E.ON, RWE, Vattenfall, EnBW
Municipal utilities
Retailers with mixed ownership structure
Small independent retailers
Electricity retail markets are regional: distribution network level.
Default supplier is the designated supplier obliged to supply any customer in their supply area (in Germany: the entity supplying the largest number of grid connection points).
Apart from the baseline contract, the default supplier can offer alternative tariffs.

## Slide 31: Categories of final customers
Industrial
Commercial
Residential
Household customers: up to 10.000 kWh yearly consumption
  residential & small commercial
  standard load profile (SLP) - approximation
Non-household customers: all other
  commercial (> 10.000 kWh yearly consumption) & industrial
  registered load profile measurement (RLM): >100 GWh p.a.

## Slide 32: Contractual set-up for electricity consumer
Contract with supplier
  Types:
    default supply
    alternative tariff with default supplier
    alternative supplier
  Typically, supplier has BRP role.
Contract with the grid operator (Network contract)
  Grid tariffs
  Metering and metering charges
Network connection contract – technical connection to the grid.
Metering responsibility:
by default – grid operator
by opt-in – independent metering company

## Slide 33: Supplier structure: Industrial and household customers
Baseline
contract with default supplier
33,20 TWh
27,8%
Alternative tariff with default supplier
49,30 TWh
41,2%
Contract with alternative supplier
37,10 TWh
31,0%
Household customers
Baseline
contract with default supplier
0,7 TWh
< 1%
Alternative tariff with default supplier
72 TWh
27%
Contract with alternative supplier
189 TWh
72%
RLM customers
Source: BNetzA, 2018

## Slide 34: Retail price composition: Household customers
Taxes and levies
Grid tariffs
(incl. metering)
Electricity
procurement,
retail
Market-based
Average composition of electricity price for a German household with an annual consumption of 3.500 kWh (2019)
Regulated
State-induced
Source: BDEW, 2019
Average price:
30,43 ct/kWh

## Slide 35: Retail price composition: Household customers
Taxes and levies
Grid tariffs
(incl. metering)
Electricity
procurement,
retail
Average composition of electricity price for a German household with an annual consumption of 3.500 kWh (2019)
Interruptible load levy (AbLaV)
Offshore levy
Levy to compensate reduced grid tariffs for certain grid users (§19 StromNEV)
CHP levy (KWK)
Green levy (EEG)
Electricity tax
Concession levy
VAT 19%
Source: BDEW, 2019
7,39 ct/kWh
7,06 ct/kWh
15,98 ct/kWh

## Slide 36: Retail price composition: Industrial consumers
Average price 2018:
8,96 ct/kWh
Source: Eurostat
Range of electricity prices for large industrial consumers with an annual consumption of 100 GWh/a:
Max. available cost relief vs. No cost relief
El. tax
KWK
Concession levy
Procureme
nt, retail
Grid tariff
Source: BDEW, 2019
(with reference to Eurostat)

## Slide 37: Retail competition
1 – 20 suppliers
21 – 50 suppliers
51 – 100 suppliers
> 100 suppliers
% of grid areas with given number of suppliers:
In almost all grid areas the number of operating suppliers is more than 20.
In approx. 90% of grid areas more than 50 suppliers are operating.
Source: BDEW, 2019 (after BNetzA, 2018)

## Slide 38: Supplier switching among household customers
Mio households
%
household customers
Souce: BDEW, 2019
Cumulated switching rate since liberalisation

## Slide 39: Retail competition: Pass-through rate
Pass-through rate is the percentage to which an electricity retailer passes on a change in their cost to their customers/ electricity consumers.

## Slide 40: Retail market: Pass-through rate
Source: Duso / Szücs, 2017
Incumbents in regional retail markets in Germany in 2010

## Slide 41: Retail market: Heterogeneity in baseline tariffs
Source: Duso / Szücs, 2017
Baseline tariff in € per MWh at 2800 kWh yearly consumption

## Slide 42: Retail market: Within-network price dispersion (2010)
Source: Duso / Szücs, 2017
Difference between baseline and best-available tariff in € per MWh at 2800 kWh yearly consumption

## Slide 43: Pass-through rate in the German retail market
Duso and Szücs / European Economic Review 98 (2017) 354-372
Summarised findings:
Supplier and customer types
Pass-through rate to baseline tariffs is quite similar across firms.
Pass-through rate to competitive tariffs is 12-23% higher for independent suppliers.
Thus, the pass-through rate depends on the customer segment, rather than supplier segment.
Time differentiation
Pass-through rates to baseline tariffs remain stable over time.
Pass-through rate to the best available tariff increases to almost unity.
Ability to switch supplier is the main driving factor for pass-through.