## Slide 1: Integrated course „Energy Economics“ - Natural Gas Markets
Prof. Dr. Boris Heinz | Dr. Elena Timofeeva
Department for Energy Systems

## Slide 2: Outline
Natural gas reserves and production
Long distance gas pipelines
Gas storage
LNG markets
Wholesale markets for natural gas
Retail gas markets

## Slide 3: Gaseous Fuels
Natural gas – mainly methane
  H gas – high-calorific natural gas (higher CH4 content → heat value)
  L gas – low-calorific natural gas (produced in GE &NL)
Liquefied petroleum gas (LPG) – mainly propane and butane, byproduct of oil refinery process
Town gas (cooking gas) – byproduct of coke plants

## Slide 4: Properties of Gaseous Fuels
© Prof. Dr. Georg Erdmann
Notes: Latent heat of vaporisation of water vapour. Same types of fuel are compared by HHV, different types of fuel – by LHV (due to different hydrogen content).

## Slide 5: Natural gas
Conventional natural gas
Extracted from gas deposits by conventional means
Associated gas – released during oil extraction (often flared but can be utilised)
Unconventional natural gas
Shale gas (>1000 m deep) – extracted by fracking
Coal bed methane – found in coal formations (300-1000 m deep)
Methane hydrates – found on ocean seabed

## Slide 6: Natural gas value chain

## Slide 7: Global Gas Resources
Source: BGR, 2013
Resources are all useful raw materials available in nature.
Reserves are resources existing with high probability and economically feasible for extraction.

## Slide 8: Reserves and extraction of natural gas
Source: Zweifel / Praktiknjo / Erdmann (2017) after BP (2014)
*
The Persian Gulf and the Caspian Sea areas
  (Bahrain, Iran, Iraq, Kuwait, Oman, Qatar, Saudi Arabia, Syria, UAE, Yemen, other Middle East;
  Azerbaijan, Kazakhstan, Russia, Turkmenistan, Uzbekistan, other Europe & Eurasia)

## Slide 9: Natural Gas in the EU
© Prof. Dr. Georg Erdmann

## Slide 10: German Gas Imports
© Prof. Dr. Georg Erdmann
Source: BAFA, 2015
[TJ]

## Slide 11: Economics of Gas Pipelines
© Prof. Dr. Georg Erdmann
Throughput is the volume of gas passing through a pipeline in a period of time.
[m3/h]
Pipeline capacity is the maximum throughput.

## Slide 12: Game Theory: Double Marginalisation
© Prof. Dr. Georg Erdmann
Gas producer is able to infer on the import price resulting from gas importer’s optimisation based on the domestic demand curve. It then optimises its profit at the given import price.

## Slide 13: Retail Gas Price set by the Monopolistic Gas Importer
© Prof. Dr. Georg Erdmann
Importer’s marginal cost = import price
(neglecting other cost elements)
Willingness to pay for the first unit = max. retail price
Linear demand function

## Slide 14: Game Theoretical View of the Gas Importer
© Prof. Dr. Georg Erdmann

## Slide 15: Game Theoretical View of the Gas Importer

## Slide 16: Game Theoretical View of the Pipeline Operator
© Prof. Dr. Georg Erdmann

## Slide 17: Game Theoretical View of the Pipeline Operator
Correction: differentiation with respect to the import price to be agreed with the gas importer.

## Slide 18: Solution under “Cooperation”
© Prof. Dr. Georg Erdmann

## Slide 19: Solution under “Cooperation”

## Slide 20: Decision of the Pipeline Investor
© Prof. Dr. Georg Erdmann

## Slide 21: Transportation Cost of Hydrocarbons
Source: Zweifel / Praktiknjo / Erdmann, 2017

## Slide 22: LNG Process Chain
Source: BV 2009 / GIIGNL
Boiling point of methane −162 °C (−259.6 °F)
Approx. 600 times volume reduction
Source: Osaka Gas

## Slide 23: Major LNG Trading Flows in 2018
Source: GIIGNL, 2019
EXPORT
IMPORT
Algeria
Australia
Brunei
Indonesia
Malaysia
Nigeria
Oman
Papua New Guinea
Quatar
Russia
UAE
USA
China
France
India
Italy
Japan
Mexico
Pakistan
Singapore
South Korea
Spain
Taiwan
Thailand
Turkey
United Kingdom
2 - 3 MT
3 - 5 MT
5 - 10 MT
>10 MT

## Slide 24: LNG Flows in 2018

## Slide 25: Cost Structure of LNG Process Chain
Source: Zweifel / Praktiknjo / Erdmann (2017), after Cayrade (2014)
Liquefaction plant: | 
Investment outlay | 900M €
Operating expenses | 0,04 €/m3
LNG tanker fleet | e.g. 2 vessels á 135T t each
Investment outlay | 360M €
Operating expenses | 0,014 €/m3
Regasification plant w. storage | e.g. 80T m3 (Cartagena)
Investment outlay | 320M €
Operating expenses | 0,015 €/m3
Own gas requirement | 1/3 of transported gas

## Slide 26: Cost Comparison of LNG Projects
Source: Songhurst, OIES, 2018

## Slide 27: LNG Impact on Global Gas Markets
LNG trade leads to integration of regional gas markets
LNG supply chain is more flexible
LNG helps to develop more remote gas fields
Diversification helps mitigate the holdup problem
Source: Zweifel / Praktiknjo / Erdmann, 2017

## Slide 28: Vertical Integration or Long-Term Contracts
© Prof. Dr. Georg Erdmann
Notes: Long-term contracts are imperfect substitute for vertical integration.

## Slide 29: Take-or-Pay Clause in Long Term Contracts
© Prof. Dr. Georg Erdmann

## Slide 30: Volume Flexibility Under Long Term Contracts (2007)
Souce: European Commission, Energy sector inquiry 2005-2006

## Slide 31: Gas storage technologies
Source: E.ON Ruhrgas
Station
Station
Observation well
Aquifer/
Production field
Porous rock storage
Cavern storage

## Slide 32: Gas storage facilities: Underground
Porous rock storage
  uses existing geological underground formations (e.g. depleted oil and gas fields)
  relatively inexpensive
  large storage volume
  more cushion gas required
  low injection and withdrawal rate
Cavern storage
  artificial hollows carved out in underground rock or salt formations
  higher investment
  less cushion gas required
  higher withdrawal rate
  fast switching between injection and withdrawal mode
  provide short-term flexibility

## Slide 33: Gas storage facilities: Above ground
LNG storage
Insulated tanks at LNG terminals
No cushion gas needed
High injection/withdrawal rates
Gas tanks
Law or high pressure
Not economical for high volumes
Local storage
Line pack
Gas stored inside pipeline through increased pressure
Used to balance daily demand fluctuations

## Slide 34: Gas storage facilities in Germany
Max. usable working gas volume as of 31.12.2018, in TWh
Total
33 storage facilities
Cavern storage
17 facilities
Porous rock storage
15 facilities
Other
1 facility
H-Gas
29 facilities
L-Gas
4 facilities
BNetzA, 2019

## Slide 35: Merchant Use of a Gas Storage
© Prof. Dr. Georg Erdmann

## Slide 36: German gas storage: Filling level development
Source: BNetzA, 2019
Range of storage filling level since 04/2011
Filling level for current storage year – as of 1 Nov 2019
Storage year 2018/19 – compared to previous years
[%]

## Slide 37: Value of gas storage
Storage buffers supply and (daily & seasonally fluctuating) demand
Value of storage is determined by the cost of alternative sources of flexibility (transportation and capacity charges):
production swing, take-or-pay, interruptible contracts, spot market
Intrinsic value
  ability to inject a certain amount of gas in summer and withdraw it in winter
  price during withdrawal minus price during injection, i.e. seasonal spread
Extrinsic value
  ability to utilise the storage volume more than once (inject and withdraw gas) during the season to profit from short-term price volatility

## Slide 38: Gas and Heating Oil Prices
© Prof. Dr. Georg Erdmann

## Slide 39: Index-based Gas Price
Souce: WINGAS
Time period in or for which (depending on the specific index type) the index is published
Part of the delivery period to the calculated price applies.
Time lag between the reference period and price applicability period
In this example: 6/1/3 rule
Typical indexation in long-term gas supply contracts: 6/3/3 rule
(6 months reference period; 3 months time lag; 3 months price applicability period)

## Slide 40: Price Indexation Under Long Term Contracts (2007)
Souce: European Commission, Energy sector inquiry 2005-2006

## Slide 41: Price Indexation by Production Region (2007)
Souce: European Commission, Energy sector inquiry 2005-2006

## Slide 42: Oil-product linked gas prices
Initial rationale for oil-based indexation is that users can choose between burning gas and oil products.
Early liberalised gas markets of the US and the UK with a liquid wholesale trading in natural gas resulted into gas-to-gas competition.
Long-term supply contracts for Continental Europe were initially linked to oil prices.
Since late 2000s European gas markets have shifted significantly from oil indexation towards hub-linked prices.
Renegotiation of price formulas in long-term supply contracts followed.

## Slide 43: Downside of Long-Term Contracts
Lacking transparency
Reduced liquidity on wholesale markets
Barrier for entry for new competitors

## Slide 44: LTC Renegotiation
Driving factors for transition to hub-linked gas prices:
US shale gas production
Qatari LNG available in Europe
Reduction in gas demand
Gas importers stayed bound by LTC at oil-linked prices incurring losses.
Renegotiation of LTC followed to introduce hub indexation.
Trends in newly signed contracts:
→ shorter duration period (10-15 years)
→ full hub indexation
→ new buyer/seller balance

## Slide 45: Evolution of TTF and German Import Contract Prices
TTF (Title Transfer Facility) – Dutch gas hub
BAFA – average German import contract
Source: Franza, CIEP (2014), with reference to DEPA

## Slide 46: Third-Party Access to Gas Infrastructure
Non-discriminatory (effective and transparent) access to gas transportation systems is a crucial prerequisite for a liquid market for natural gas.
Unbundling for gas TSOs (see EU Gas Directive 2009/73/EC):
Transmission and distribution activities are separated from the rest of the value chain
Ownership unbundling
Independent system operator (ISO)
Independent transmission operator (ITO)
Certification to ensure compliance with unbundling requirements for transmission system owner or TSO controlled by person(s) from third country(ies)
„Gazprom clause“
See lecture 11
on unbundling: equivalent rationale and requirements apply for the gas sector.

## Slide 47: Gas Network Access Models
Point-to-point system
gas traders book specific transportation route from an entry to an exit point
distance-based capacity pricing
Entry-exit system
entry and exit capacities are booked separately
entry fee and exit fee – capacity pricing independent of distance
traders with entry capacities can sell gas to traders with exit capacities
each exit point can be supplied from any entry point
Entry-exit system enables wholegas gas trading on virtual trading point (virtual hub) / market area level: gas is traded independently of its location in a market area.

## Slide 48: Key Elements of Network Access Model
Non-discriminatory network access to facilitate competition
Capacity and congestion management
Allocation principles
Capacity products
Further rules/incentives
Balancing
Balancing period
Imbalance pricing
Flexibility market
General network access model
Entry-exit
Point-to-point
Postage stamp
Overall
objective
Areas of
network
access
Options/
major
determinants
Source: Hewicker & Kesting, in: Handbook Utility Management, 2009
Notes: In point-to-point model imbalance under each contract is priced.
In entry-exit model net imbalance is considered.

## Slide 49: Point-to-point Model
Exit
Entry
Source: Hewicker & Kesting, 2009
Network
Contract Path
Shippers specify entry and exit points and the transportation path.
Actual physical flow may differ from the contracted path.
Entry and exit capacities cannot be separated from each other and from the gas (commodity) transaction.

## Slide 50: Entry-exit Model
Exit
Exit
Entry
Entry
Exit
Entry
Source: Hewicker & Kesting, 2009
Exit
Shippers book entry and exit capacity independently from each other.
No need to specify transportation path or distance.
Contracts for entry and exit capacities are independent from each other and from commodity transactions.
Entry and exit tariffs are set independently for each entry/exit point
Different tariffs for each point
All network operators in a network zone cooperate and set tariffs on a cost-reflective basis.
5
10
10
12
5
7
4
Notes: Point-specific tariffs should, ideally, reflect the cost of capacity extension required to eliminate congestion.

## Slide 51: European gas regions, markets and hubs
Source: OIES (2017) with reference to www.worldatlasbook.com and P. Heather

## Slide 52: Gas Hubs
Physical gas hub, e.g.
Henry Hub (USA) – connecting point of 14 pipelines
Zeebrugge (Belgium)
Baumgarten (CEGH, Austria)
Virtual gas hub, e.g.
NBP, National Balancing Point (UK)
TTF, Title Transfer Facility (Netherlands)

## Slide 53: Physical gas hubs: Baumgarten
Source: Heather, OIES (2012) with reference to CEGH Exchange
Major physical pipeline interconnection point in the near Slovakian border
13 physical locations (flanges)
Wheeling services provided by CEGH
1/3 of gas imports from Russia to Western Europe

## Slide 54: Virtual Gas Hubs: Austrian Virtual Trading Point (VTP)
Source: Heather, OIES (2012) with reference to E-Control

## Slide 55: Forms of Gas Trading
Motivations to trade:
Balancing physical portfolio (asset-backed)
Financial hedge
Speculation (merchant/proprietary)

## Slide 56: Forms of Gas Trading

## Slide 57: Comparison Electricity – Gas
Electricity Market
Transmission system operator (TSO)
Balance group coordinator
Distribution system operator (DSO)
Control area
BG per control area
Balance Responsible Party (BRP)
SLP and RLM customers
Symmetrical imbalance price
Gas Market
Transmission system operator (TSO)
Market area coordinator (NCG, Gaspool)
Regional and local system operators (DSO)
Market area / Virtual trading point
BG per market area
Balance Responsible Party (BRP)
SLP and RLM customers
Positive and negative imbalance price

## Slide 58: Structure of the Value Chain
© Prof. Dr. Georg Erdmann

## Slide 59: Companies Along the Value Chain
© Prof. Dr. Georg Erdmann

## Slide 60: Incumbent’s standard gas offers for households in EU capitals – Nov/December 2018 [%]
Source: ACER/CEER, 2018

## Slide 61: Pass-through in gas retail market at EU level
Responsiveness of the energy component of the retail prices to changes in wholesale prices and evaluation of mark-ups in the household segments from 2012 to 2018
Source: ACER, 2018