## Slide 1: Integrated course „Energy Economics“ - Markets for CO2 Emission Allowances
Chair of Energy Systems
Prof. Dr. Boris Heinz | Dr. Elena Timofeeva
elena.timofeeva@tu-berlin.de

## Slide 2: Outline
External costs
Quantification of external costs
Greenhouse gas problem
European Cap-and-Trade system

## Slide 3: Task 1) External costs and internalisation
Explain the term externality in the context of GHG emissions.
Externality describes the impact of economic activities on outsiders without compensation. The external effect can be either positive or negative. GHG emissions are associated with a negative externality.
b) Why does the externatily of GHG emissions lead to insufficient energy markets?
If the external effect of GHG emissions was not included into energy prices, the polluter (e.g. operator of a power plant) would choose a profit optimising production level. By reducing his production he would be less badly off (makes less profit) than the damaged party better off (suffer less from GHG emissions). Therefore, we don’t have a Pareto-optimal market outcome (market failure). See next slide.

## Slide 4: Optimal Emmision Levels
Profit Π
External Costs Cext
Emissions Em
Π0
Em0
Π*
Cext,0
Em*
0
Profit Π
External Costs Cext
Maximize

## Slide 5: Marginal Damages and Marginal Abatement Costs
Marginal Profits,
External Marginal Costs
Em0
Em*
0
Emissions Em

## Slide 6: Task 1) External costs and internalisation
c) Which policy instruments can correct this market failure in energy markets?
Emissions standard and norms (cap)
Emissions tax (Pigou tax)
Cap-and-trade system
The reason why a cap-and-trade system needs trade (and is not only a cap system) is that the govenment does not know the optimal cap for every installation (lack of information on the abatement costs of every company). Thus, the allocation of certificates is necessarily not optimal. If companies can trade the certificates, the same overall amount of emissions will be abated but at lower costs.
d) Explain the quantity risk and price risk in the context of these policy instruments.
With a tax system there is price stability. However, as the government lacks information about the shape of the marginal abatement cost function, there is no security of reaching the reduction target (quantity risk). If the tax is too low, emissions will be too high; if the tax will be too high, the emissions will be too low. Resulting costs of the companies are uncertain.
With a cap-and-trade system there is security of reaching the emissions target. However, as the government lacks information about the shape of the marginal abatement cost function, there is insecurity about the price of CO2 emission certificates (price risk) and about resulting costs for the companies. See next slides.

## Slide 7: GHG Abatement Costs and a Pigou Tax
[Euro/t CO2]
CO2 emissions
Starting point
Marginal GHG abatement costs

## Slide 8: GHG Abatement Costs under Cap and Trade
[Euro/t CO2]
CO2 emissions
Starting point
Marginal GHG abatement costs

## Slide 9: International Framework on Climate Change
1979 World Climate Conference in Geneva
1988 UN Weltklimarat (Intergovernmental Panel on Climate Change, IPCC)
1992 (1994) UN Klimarahmenkonvention (UNFCCC)
Annex I countries: Industrialised countries that have agreed to reduce their greenhouse gas emissions
Annex II countries: Developed countries that are responsible for bearing the costs of climate change mitigation in developing countries (subset of Annex I countries)
Developing countries: These countries have no immediate responsibilities.
1999 (2005) Kyoto Protocol to UNFCCC
Binding CO2 reduction targets:
1st commitment period 2008-2012
2012 Doha Amendment: 2nd commitment period 2013-2020
COP – annual Conference of Parties to UNFCCC
Notes: Countries have common but differetiated responsibilities.

## Slide 10: Kyoto Protocol
Greenhouse gases:
Sector and source categories:
Energy
Industrial processes
Solvents and other product uses
Agriculture
Waste
+ Impact of Land-Use, Land-Use Change and Forestry (LULUCF)

## Slide 11: The Greenhouse Gas Problem [Data Source IPCC 1990; 2014]
 | Carbon dioxide CO2 | Methane CH4 | Nitrous oxide N2O
Pre industrial concentration [ppmv] | 280 | 0.7–0.8 | 0.23
Average atmospheric lifetime [years] | 5–200 | 9-15 | 120
Global warming potential in 20 years | 1 | 72 | 289
Global warming potential in 100 years | 1 | 25 | 298
Contribution to the GHG problem [%] | 77 | 14 | 8
Reduction target of the IPCC 1990 [%] | 60–80 | 15–20 | 70–80

## Slide 12: Committed Emission Limits under Kyoto Protocol
Source: Burger / Graeber / Schindlmayr (2014)

## Slide 13: Kyoto Protocol: Flexible Mechanisms
Cost-effective options for reducing emissions or removing CO2
in other countries
Clean Development Mechanism
Project-based reduction of CO2 emissions between non-Annex 1 countries and Annex 1 countries
Emission reductions must be additional (compared to baseline).
Independent certification
Joint Implementation Mechanism
Project-based reduction of emissions between two Annex 1 countries
International Emissions Trading
Emissions trading among Annex B countries
Not in use

## Slide 14: Emission Allowances: Terminology
AAU: Assigned Amount Unit or Kyoto unit. An AAU permit to emit 1 t of CO2 or 1 t CO2 equivalent of greenhouse gases.
ERU: Emission Reduction Unit. An ERU is a certified emission reduction of 1 t of CO2 resulting from a Joint Implementation project.
CER: Certified Emission Reduction. A CER is a certified emission reduction of 1 t of CO2 resulting from a CDM project.
EUA: EU Allowance. An EUA permit operators of an industry installation or electricity generation unit to emit 1 t of CO2 under the EU emissions trading system.
EUAA: EU Aviation Allowance. An EUAA permit airlines to emit 1 t of CO2 under the EU emissions trading system.

## Slide 15: GHG-Emissions in the EU-27 [Source EEA 2009]
Unilateral target: -20% in 2020 compared to 1990
Source: European Environment Agency EEA 2009

## Slide 16: EU-27 Composition of GHG Emissions 2007 [Source EEA 2009]
(*) 24 % with intl. aviation and intl. maritime navigation

## Slide 17: EU Emission Trading System (ETS)
For tax issues all EU member states must agree, but majority vote is sufficient for ETS system
Mandatory “CO2 Cap and Trade” system for
  Installations of power, refinery, steel, glass, cement industries (2071 mio t CO2 verified emissions in 2005)
  airline business (after 2011)
EU wide annual cap of tradable CO2 Allowances (EUA)
Almost free allocation of emission rights in the first two trading periods 2005/7 and 2008/12  Windfall profits
System is intended to become the prototype for a global “cap and trade” system

## Slide 18: Emission Allowances and Abatement Cost
Abatement cost of company 1 (marginal cost)
CO2 emissions
Emissions of company 1
Alllocated emissions Em1
Emission reduction requirements for company 1

## Slide 19: Trade of Emission Allowances
CO2 Emissions
CO2 Emissions
Emission right EM2
Abatement cost of company 2
Reductions of company 2
Abatement cost of company 1
Emission right EM1
Reductions of company 1
ARBITRAGE

## Slide 20: Trade of Emission Allowances
Effects of the trade:
The given emissions target can be attained at a lower cost.
At a given cost, a more ambitious emissions target can be achieved.

## Slide 21: Designing Emissions Trading System
Trading period length:
If the trading period is too long, the incentives are weak.
If the trading period is too short, there is lack of certainty for investments.
Allocation of emissions allowances:
Grandfathering – free allocation → windfall profits
  CO2 prices are opportunity costs of power plant operators (as certificates could be sold instead of covering emissions from electricity production) and, thus, included into the product price anyway, even if emission allowances are received for free.
Auctioning – operators buy allowances in auctions.
  Government collects and redistributes auctioning revenues.
  In the EU: min 50% for climate and energy related purposes

## Slide 22: Trade of Emission Allowances
Abatement cost of company 2 (marginal cost)
Emission trade
Abatement cost of company 1 (marginal cost)
Allocated rights
ARBITRAGE

## Slide 23: Task 3) CO2 Reduction in Lummerland
The island of Lummerland wants to reduce its CO2-emissions by 100 000 tons per year. The industry on the small island consists basically of two main types: castle construction and production of steam engines. Both industries have different CO2-reduction goals with different abatement costs.
Industry A: Castle construction (incl. energy-intensive cement production)
CO2-reduction goal: 40 000 tons per year CO2-abatement costs per year:
Industry B: Production of steam engines (incl. energy-intensive steel melting)
CO2-reduction goal: 60 000 tons per year CO2-abatement costs per year:

## Slide 24: Task 3) CO2 Reduction in Lummerland
What are the abatement costs per ton CO2 for Industry A?

## Slide 25: Task 3) CO2 Reduction in Lummerland
What are the abatement costs per ton CO2 for Industry B?

## Slide 26: Task 3) CO2 Reduction in Lummerland
In order to lower the costs for CO2 abatement, the government of Lummerland introduces a new emissions trading mechanism. What is the theoretical volume traded?
Find the volume at which the marginal abatement costs of both industries are equal.
Given functions are for annual abatement costs as a function of the annual amount of CO2 reduction.
Total required reduction for both industries is 100.000 tons.

## Slide 27
Second root does not meet the condition (just a matematical solution).
Under perfect market conditions 66.123 t CO2 will be abated by industry A.
The difference between industry A’s abated amount and its reduction target will be traded.

## Slide 28: Task 3) CO2 Reduction in Lummerland
What is the system price in the emissions trading system?
What are now the overall abatement costs per ton CO2 for Industry B?
To be continued