## Slide 1: Energy Economics - Plenary Tutorial 1. Microeconomics / Economic Fundamentals
David Schröder | Department for Energy Systems david.schroeder@tu-berlin.de

## Slide 2: Organisational topics
Exam: Tuesday, 26.02.2019 11 – 14 hrs at H104
  Registration until 19.02.2019
  Withdrawal until 25.02.2019
Lecture on Tuesday, 29.01.2018

## Slide 3: Questions on the previous tutorials
?

## Slide 4: Brief theoretical summary of the topic
Categories of Costs in Power Production
Load Curve and Load Duration Curve
Residual Load
Merit Order
  Merit Order Effect of Renewables
  Impact of CO2 – Prices
  Windfall Profit of CO2 - Prices

## Slide 5: Categories of costs in power production and their relevance
 | Relevency for |  | 
 | Operational Decisions | Decommissioning Decisions | Investment and Expansion Decisions
Costs depending on capacity | [€/MW] |  | 
Capital costs (annuity) Labour costs Fixed O&M costs |  |  | 
Costs depending on operation | [€/MWh] |  | 
Fuel costs CO2 costs Other variable costs (e.g variable O&M costs, ramping costs, start-up costs) |  |  | 

## Slide 6: Load Curve and Load Duration Curve
1
2
4
3
Pmax
Pmin
P[MW]
Time of day
4
1
2+3
P[MW]
Cumulative hours
Load Curve
Load Duration Curve

## Slide 7: Load and Residual Load
Chart: Load Duration Curve – schematic illustration
Load
reduced by must-run
(RES, inflexible conventional technologies)
Residual Load
Surplus
applicable for
storage charge
additional consumption: intersectoral technologies
to be covered by
adjustable generation
storage discharge
Demand

## Slide 8: Merit Order
Oil
Coal
Gas
Nuclear
Hydro
Marginal costs
Installed Capacity
Notes: The merit order is a way of ranking available sources of energy, especially electrical generation, based on ascending order of price (which may reflect the order of their short-run marginal costs of production) together with amount of energy that will be generated. In a centralized management, the ranking is so that those with the lowest marginal costs are the first ones to be brought online to meet demand, and the plants with the highest marginal costs are the last to be brought on line. Dispatching generation in this way minimizes the cost of production of electricity

## Slide 9: Merit Order
Oil
Coal
Gas
Nuclear
Hydro
Marginal costs
Installed Capacity
Load
Notes: The merit order is a way of ranking available sources of energy, especially electrical generation, based on ascending order of price (which may reflect the order of their short-run marginal costs of production) together with amount of energy that will be generated. In a centralized management, the ranking is so that those with the lowest marginal costs are the first ones to be brought online to meet demand, and the plants with the highest marginal costs are the last to be brought on line. Dispatching generation in this way minimizes the cost of production of electricity

## Slide 10: Merit Order Effect of Renewables
Oil
Coal
Gas
Nuclear
Hydro
Marginal costs
Installed Capacity
Load
Renewables
Notes: Merit Order Effect of the Renewables can be shown by changing the load curve or the generation curve.
In this case: Load is uncanged, Renewables shift the conventional merit order to the right, since they have the lowest marginal generation costs.
The merit order effect of renewable energy sources (RES) describes the impact of feed-in of renewable (must run) electricity on electricity prices. As renewable electricity feed-in such as wind or photovoltaic virtually comes at zero costs, the demand for conventional generation capacity is reduced by the amount of renewable feed-in. As a result the prices for electricity decrease: the merit order effect

## Slide 11: Merit Order
Oil
Coal
Gas
Nuclear
Hydro
Marginal costs
Installed Capacity
Load
Renewables
Residual Load
Notes: Residual Load = Load of consumers, reduced by RES, and inflexible must-run capacities

## Slide 12: Merit Order - Impact of CO2 – Prices
Oil
Coal
Gas
Nuclear
Hydro
Marginal costs
Installed Capacity
Load
CO2-Price
CO2-Price
CO2-
Price
Windfall-
Profit
Windfall-Profit
Notes: CO2-Price has to be priced into the marginal generation costs. Thereby changing the merit order.
There is a CO2 price at which generation technologies switch position in the merit order.

## Slide 13: Task 1) Load Duration Curve
The peak load in a power system is 16 000 MW. Other load values and their durations in a year are given in the table.
Sketch a load duration curve.
What are the limitations of electricity market analyses based on a load duration curve?
What is the so called “residual load” and what does it imply?
Load [MW] | Duration [h]
≥ 12 000 | 1 500
≥ 8 000 | 4 500
≥ 6 500 | 7 000
≥ 4 000 | 8 760

## Slide 14: Task 1) Load Duration Curve
The peak load in a power system is 16 000 MW. Other load values and their durations in a year are given in Table 1.
Sketch a load duration curve.
Load [MW] | Duration [h]
≥ 12 000 | 1 500
≥ 8 000 | 4 500
≥ 6 500 | 7 000
≥ 4 000 | 8 760
Chart: Hours of the year
| Load [MW] | Hours of the year
 | 0 | 0

## Slide 15: Task 1) Load Duration Curve
The peak load in a power system is 16 000 MW. Other load values and their durations in a year are given in Table 1.
What are the limitations of electricity market analyses based on a load duration curve?
What is the so called “residual load” and what does it imply?

## Slide 16: Task 2) Merit Order and Dispatch Decisions
Which categories of costs in the power sector are relevant i) for operational decisions ii) for decommissioning decisions and iii) for investment decisions? Explain why!
Assume the power plants given in table 2 have been constructed already. Sketch the merit order for these power plants. What is the electricity price at a load of 1.7 GW?
Now assume that there is a CO2 trading system. Calculate the emissions price (€/t CO2) at which the coal fired units show the same short-term marginal generation costs as the gas fired ones.
Notes: a) See slide 5

## Slide 17: Task 2) Dispatch Decisions
Assume the power plants given in table 2 have been constructed already. Sketch the merit order for these power plants. What is the electricity price at a load of 1.7 GW?

## Slide 18: Task 2) Dispatch Decisions
Assume the power plants given in table 2 have been constructed already. Sketch the merit order for these power plants. What is the electricity price at a load of 1.7 GW?
Chart: Cumulative Capacity [MW]
| Load [MW] | Hours of the year
 | 0 | 0

## Slide 19: Task 2) Dispatch Decisions
Now assume that there is a CO2 trading system. Calculate the emissions price (€/t CO2) at which the coal fired units show the same short-term marginal generation costs as the gas fired ones.

## Slide 20: Task 3) Merit Order Effect of Renewables
The installed capacity of conventional generation capacity (i.e. capacity that can be dispatched) in a given power system is 80 GW. The corresponding merit order can be approximated by the following supply function: , where are the marginal generation costs in €/MWhel and the cumulated capacity in GW. The demand for peak load power is given by , where is the load demand in GW as a function of the electricity price .
What is the equilibrium price and load in the given example?
Assume there is additional supply of wind power. Furthermore, assume that the feed-in of wind power is 10 GW. What is the impact on electricity prices?
What is the so called merit order effect of renewable energy sources?
How does the merit order effect influence the profit of large scale wind power or other intermittent resources?

## Slide 21: Task 3) Merit Order Effect of Renewables
The merit order can be approximated by the following supply function:
The demand for peak load power is given by
What is the equilibrium price and load in the given example?

## Slide 22: Task 3) Merit Order Effect of Renewables
The merit order can be approximated by the following supply function:
The demand for peak load power is given by
Assume there is additional supply of wind power. Furthermore, assume that the feed-in of wind power is 10 GW. What is the impact on electricity prices?

## Slide 23: Task 3) Merit Order Effect of Renewables

## Slide 24: Task 3) Merit Order Effect of Renewables
What is the so called merit order effect of renewable energy sources?
How does the merit order effect influence the profit of large scale wind power or other intermittent resources?
Notes: c) See slide 11

## Slide 25: Supplementary practise material I Power plants and CO2 - Prices
The installed capacity of conventional generation capacity (i.e. capacity that can be dispatched) in a given power system is 80 GW. The corresponding merit order can be approximated by the following supply function: , where are the marginal generation costs in €/MWhel and the cumulated capacity in GW. The demand for peak load power is given by , where is the load demand in GW as a function of the electricity price .
What is the equilibrium price and load in the given example?
Assume there is additional supply of wind power. Furthermore, assume that the feed-in of wind power is 10 GW. What is the impact on electricity prices?
What is the so called merit order effect of renewable energy sources?
How does the merit order effect influence the profit of large scale wind power or other intermittent resources?

## Slide 26: Supplementary practise material I Power plants and CO2 - Prices

## Slide 27: Supplementary practise material II Screening Curve
As a consulting engineer you are asked to determine the optimal, i.e. cost minimal, mix of power plants for a given power system. The different options including their techno-economic properties are given in table 3. The load duration curve can be approximated by the following function: LDC(t)=25 000-t, where LDC(t) is the load in MW and t the hours of duration.

## Slide 28: Supplementary practise material II Screening Curve
As a consulting engineer you are asked to determine the optimal, i.e. cost minimal, mix of power plants for a given power system. The different options including their techno-economic properties are given in table 3. The load duration curve can be approximated by the following function: LDC(t)=25 000-t, where LDC(t) is the load in MW and t the hours of duration.
What are the (short-term) marginal generation costs of the respective units?
What are the annual capital costs?
What are the total annual fixed costs per MW installed?
Make a graph which plots the so called linear screening curves of the respective technologies.
What is the peak load in the system?
Calculate the optimal shares of capacity for the respective units.
Due to the feed-in of wind energy, the load duration curve changes as follows:
  What is the capacity credit of wind energy?
  Calculate the new optimal capacity shares.

## Slide 29: Supplementary practise material II Screening Curve